## Slide 1: EDES 301 Responsive Path Lighting Proposal
2026/09/30
Kathy Xu

## Slide 2: Background Information
As an architecture student, I am interested in how lighting can guide movement and shape spatial experience. Instead of treating circulation lighting as a static condition, this project explores how light can respond directly to a person moving through a space, illuminating only the areas currently being used.
What is being proposed?
  A lighting system that responds to a person moving through a circulation space.
  Four sensing zones detect the user’s position along a path.
  Each sensor controls a corresponding lighting zone.
  Lights activate sequentially as the user moves through the space.
  Lighting can fade/dim after the user leaves a zone.

## Slide 3: Background Information

## Slide 4: Background Information
What improvements / additions over existing project
  Link: https://docs.waveshare.com/ESP32-Arduino-Tutorials/13-3-Presence-Light
  expands from 1 motion sensor and 1 lighting zone to 4 of each
  Adds sequential lighting, so different zones activate as a person progresses along the path.
  Adds graduated brightness / fading, allowing nearby zones to remain dim while the occupied zone is brightest.
  Adds movement through space as the design concept

## Slide 5: System Block Diagram
HC-SR501 PIR
Sensor 1
Zone 1
HC-SR501 PIR
Sensor 2
Zone 2
HC-SR501 PIR
Sensor 3
Zone 3
HC-SR501 PIR
Sensor 4
Zone 4
PocketBeagle
Python Program
Read sensors
Identify zone
Lighting logic
Fade/delay light
Level Shifter
(3.3V  5V data)
WS2812B LED
Strip 1
Zone 1
WS2812B LED
Strip 2
Zone 2
WS2812B LED
Strip 3
Zone 3
WS2812B LED
Strip 4
Zone 4
GPIO
GPIO
GPIO
GPIO
GPIO / digital data
WS2812B data line

## Slide 6: Power Block Diagram
5V USB Power
PocketBeagle
5V out
3.3V
HC-SR501 ×4
PIR Sensors
5V Supply
WS2812B ×4
LED Strips
5V Supply
Level Shifter
Logic Side
3.3V Supply
Common ground

## Slide 7: Components / Budget
Component | EDES301 to Buy? | Cost
HC-SR501 motion sensors (4) | yes | $7.91
Bidirectional level shifters (1) | yes | $1.60
BTF-LIGHTING WS2812B IC PC Light Strip | yes | $17.99
PocketBeagle | no | provided
Breadboard / Jumper Wires | no | provided
USB Power Supply / Cable | no | provided
Total |  | $27.50

## Slide 8: Power Block Diagram
Create a Power Block Diagram
  Label voltages / currents of components
Need All Power Inputs and Outputs

## Slide 9: System Block Diagram
Create a System Block Diagram
  Label interfaces (I2C, SPI, GPIO, etc.; You do not need to know all of the connections)
  Components (part numbers if possible)
Need Moderate Level of Detail

## Slide 10: Component Selection (Remove slide for submission)
All components must be from either: Amazon, Adafruit, Sparkfun, Digi-Key, or Mouser
Select no more than two (2) components that are not on approved component spreadsheet
  See Canvas  Files  assignments  EDES301_project_01_parts_list.xlsx
  If there is a cheaper part that you would like to use, we can discuss in the project meeting
All components needed for the project should be listed on Slide 5
All components should have links to the website where they can be purchased
  Please trim URLs for links to Amazon
EDES301 will supplement $25 to $35 dollars for components
  Please indicate what components need to be purchased by EDES301
If you have a special request, we can discuss in the project meeting