## Slide 1: EDES 301 Responsive Path Lighting Proposal
2026/09/30
Kathy Xu

## Slide 2: Background Information
As an architecture student, I am interested in how lighting can guide movement and shape spatial experience. Instead of treating circulation lighting as a static condition, this project explores how light can respond to both people moving through a path and changing environmental conditions, using brightness and color to create a more responsive outdoor space.
What is being proposed?
  A responsive outdoor circulation lighting system that reacts to movement and environmental conditions.
  Three VL53L0X distance sensors detect a user’s position and proximity along a path.
  Each sensor controls a corresponding lighting zone.
  Lights intensity changes according to the user’s distance from each zone.
  Temperature data influence the color of the lighting.
  Time of day adjusts the baseline lighting level.

## Slide 3: Background Information

## Slide 4: Background Information
What improvements / additions over existing project
  Link: https://learn.adafruit.com/adafruit-vl53l0x-micro-lidar-distance-sensor-breakout/python-circuitpython
  Expands from basic distance-sensor reading to three sensing zones along an outdoor circulation path.
  Uses distance measurements to control lighting intensity, rather than only displaying or printing distance values.
  Adds temperature as a second environmental input that controls lighting color.
  Adds time-of-day behavior to modify the overall lighting mode or brightness.

## Slide 5: System Block Diagram
VL53L0X
Sensor 1
Zone 1
VL53L0X
Sensor 2
Zone 2
HC-SR501 PIR
Sensor 3
Zone 3
PocketBeagle
Python Program
Read distance
Read Temperature
Identify zone
Set Brightness
Set color
Fade/timing
Level Shifter
(3.3V  5V data)
WS2812B LED
Strip 1
Zone 1
WS2812B LED
Strip 2
Zone 2
WS2812B LED
Strip 3
Zone 3
I2C
I2C
I2C
GPIO / digital data
WS2812B data line
Temp/Humidity Sensor
I2C

## Slide 6: Power Block Diagram
5V USB Power
PocketBeagle
5V in
3.3V
VL53L0X ×3
Distance Sensors
3.3V Supply
WS2812B ×4
LED Strips
5V Supply
Level Shifter
Logic Side
LV = 3.3V
Common ground
AHT10
Temp/Hum. Sensor
3.3V Supply
Level Shifter
Logic Side
HV = 5V

## Slide 7: Components / Budget
Component | EDES301 to Buy? | Cost
VL53L0X Distance Sensors (3) | yes | $8.99
AHT10 Temp/Humidity Sensor | yes | $1.70
Bidirectional level shifters | yes | $1.60
BTF-LIGHTING WS2812B IC PC Light Strip (3) | yes | $13.49
PocketBeagle | no | provided
Breadboard / Jumper Wires | no | provided
USB Power Supply / Cable | no | provided
Total |  | $25.78